## Slide 1: LTE Router
TROUBLESHOOTING guide
BandLuxe R50X

## Slide 2: BASIC SET-UP

## Slide 3: BASIC SET-UP

## Slide 4: BASIC SET-UP
Connecting the External Antenna
Connector: SMK TS9

## Slide 5: BASIC SET-UP
SIM Card
SIM Card is detected
Have to be active
SIM card can be detected by BandLuxe LTE router.
(You can view this on the OLED Screen)
SIM Card is not detected

## Slide 6: BASIC SET-UP
SIM Card
Check signal strength:
(You can view this at the upper-left part
Of OLED screen)
No Signal
Good Signal

## Slide 7: BASIC SET-UP
Device
Check device radio access network
(You can view this on the left of the device)
GSM/GPRS
LTE
HSPA/HSPA+
WCDMA
EDGE

## Slide 8: BASIC SET-UP
Device
-Log In
Default IP address (http://192.168.1.1)
URL (http://R500.ROUTER)
Default User Name and Password
are user | (leave the password as blank)

## Slide 9: BASIC SET-UP
Device
Check Network Set-Up:

## Slide 10: BASIC SET-UP
Device
Check Access Point Name (APN):

## Slide 11: BASIC SET-UP
Device
-WiFi
Default Network Name(SSID) is LTE_ROUTER,
network security key is last 8 digits of WLAN MAC
If failed, log into the R500 to change WiFi setting
or restore to factory default setting.

## Slide 12: NO INTERNET CONNECTION
SIM Card can’t be detected /No Signal
Remove then re-insert SIM Card in the router.
If No Signal, Change Radio Settings based on your internet activity:
If Poor Signal, change location of router to another area

## Slide 13: NO INTERNET CONNECTION
Ensure that correct Access Point Name (APN) supplied by the SIM card carrier.
Make sure that your signal is stable
Can not
connect to internet.
If it’s roaming, set “Roaming connection” as Enabled

## Slide 14
Temporarily turn off anti-virus and firewall.
The anti-virus and firewall might be the possible cause.
Check signal
Slow internet connection
Check there’s only one user using the router
(ex: Set Maximum number of users to “1”…)

## Slide 15
Slow internet connection
Check computer specifications:
Recommended specifications:
Pentium IV or higher
512 MB of RAM or higher
USB 2.0 port
50 MB free disk space

## Slide 16: VPN
The default IP Address of BandLuxe R500 is 192.168.1.1
If the VPN fails, make sure that the segment of R500's IP is not overlap with the company’s.
i.e. If the IP address of the company Server is 192.168.1.1
then, configured the IP address of BandLuxe R500 to 192.168.x.x

## Slide 17: Install and Configure problem
Hardware connection:
1. Check if the Ethernet cable connecting between the PC-Ethernet and R500-LAN port
2. Check if the Ethernet cable is working
- Why can't I link on the R500 GUI
PC’s setting:
1. Go to Start > Control Panel > Network and Internet >
Network and Sharing Center > Change adapter settings
2. Right click on the Local Area Connection and select Properties
3. Select Internet Protocol Version 4 (TCP/IPv4) from the list of
items and click Properties.
4. Ensure the radio buttons beside Obtain an IP address
automatically is selected. Click OK.

## Slide 18: Knowing the R500 version
1. Go to Status > Router
2. In Firmware Information, the Firmware version and Modem Version displayed here.

## Slide 19: End
BandRich Inc.